## Slide 1: Flexible water infrastructure planning under climate change uncertainty in Mombasa, Kenya
Modeling approach, results, and validation for climate, hydrology, and reservoir design
Sarah Fletcher and Megan Lickley

## Slide 2: Hydrological modeling data
Data:
  Streamflow: 1 gauge, monthly data from 1976-1990. Some missing data points filled in by gov’t study.
  P: CRU data for grid cells near Mombasa
  T: CRU data for grid cells near Mombasa
Notes
  Casey’s study and gov’t study use local rain gauge data. We use the CRU data to be consistent with the CMIP-5 projections. This leads to some differences in hydrological model.
Notes: Meg - What is the size of grid cells? And what is the motivation for using 9 of them again?

## Slide 5: Hydrological model: CLIRUN II
Designed for climate change impacts on runoff
Lumped watershed, two-layer
Inputs: T, P, PET
Calibrated by minimizing square error to observed runoff, subject to constraints on the parameter values

## Slide 6: PET Calculated using Modified Hargreaves
Validation: Matches CRU PET data well
Each panel in plot is one year from 1976 to 1990
Tmax – Tmin difference assumed to be the same even in future climates. We could investigate sensitivity of this assumption.

## Slide 7: CLIRUN calibration
The search algorithm used is approximate and sensitive to initial values; a range of initial values was used to compare different calibration performance
Given the limitations of the streamflow data, we also tested using Princeton Drought Monitor data to see if better calibration performance could be achieved. This streamflow data is modeled data using CRU P and T data.
Validation: All of the streamflow was used in the calibration given the limited data. The calibration was verified by comparing MAR and estimated firm yield to two previous studies.

## Slide 8: CLIRUN Calibration
Lowest RMSE of all attempts
Uses measured gauge
Good visual match of both peaks and monthly averages
Parameter values reasonable – Ken, yes?
mm/d

## Slide 9: Calibrated CLIRUN parameters
 | sat | lm | ku | kp | kl | inter | over
Upper bound | 200 | 200 | 1.9 | .3 | .5 | 1.1 | .3
Lower bound | 2 | 2 | .001 | .0001 | .001 | .6 | .01
Calibrated | 4.125 | 53.95 | 0.148 | 0.215 | 0.00121 | 0.625 | 0.16875
Ken – perspectives on this?

## Slide 10: Firm yield estimates
Used sequent-peak algorithm

## Slide 11: Validation comparing BMA time series to historical